## Slide 2
A collaborative initiative during pre-monsoon 2020

## Slide 3: We 40 organizations together collected pre monsoon 2020 water level (12 states, 330 blocks and 17200+ wells)
https://wmt.indiaobservatory.org.in
Outcomes:
Captured local variation of water level
Higher granularity in data
Identified local Recharge and Discharge zone
Identified ground water flow path and contour
Depth to water from surface to access water
Higher accuracy in DST for soil and water conservation

## Slide 4
One example: Comparison of Ground Water Data in Rajasthan (CGWB and WMT data)
CGWB (2007-17)= 1049 wells (326sqkm/well)
Well Monitoring Tool 2020 = 6014 wells (12 districts)
Water Monitoring Tool Data, 2020 Pre Monsoon |  |  | 
District | Geographic Area (sqkm) | No of Wells | Area (sqkm)/Well
Bhilwara | 10509 | 2098 | 5.0
Chittaurgarh | 7822 | 581 | 13.5
Udaipur | 11724 | 524 | 22.4
Pratapgarh | 4117 | 1325 | 3.1
Sirohi | 5136 | 301 | 17.1
Ajmer | 8481 | 59 | 143.7
Barmer | 28387 | 127 | 223.5
Rajsamand | 4551 | 231 | 19.7
Tonk | 7194 | 106 | 67.9
Dungarpur | 3770 | 86 | 43.8
Pali | 12387 | 405 | 30.6
Jaipur | 11152 | 71 | 157.1
Average Area (sqkm)/Well |  |  | 62.3

## Slide 5
Well Monitoring Tool = 2090 wells (5.02 sqkm/well)
Zoom to Ground Water Data in Bhilwara district of Rajasthan
CGWB = 38 wells (276 sqkm/well)

## Slide 6
Bijoliya
Jahazpur
Kotri
Shahpura
Banera
Bhilwara
Mandal
Raipur
Sahara
Asind
Hurda
Mandalgarh
Water Table
518
Elevation wireframe

## Slide 7
Good Recharge Zone
Moderate Recharge Zone
Discharge Zone
Jahazpur
Kotri
Shahpura
Banera
Bhilwara
Mandal
Raipur
Sahara
Asind
Hurda
Mandalgarh
Water Table
Bijoliya
Drainage System in Bhilwara
N
Ground Water flow path

## Slide 8
Jahazpur
Kotri
Shahpura
Banera
Bhilwara
Mandal
Raipur
Sahara
Asind
Hurda
Mandalgarh
Bijoliya
Recharge potential map based on CGWB data
Ground water flow and Recharge potential based on WMT data

## Slide 9
CGWB data wise water table of Bhilwara district
WMT data wise water table of Bhilwara district
WMT data at a higher resolution showing local variation of ground water regime

## Slide 10
Pre monsoon Ground Water flow of Mandalgarh Block

## Slide 11
Recharge potentiality based on Pre monsoon Ground Water flow of Mandalgarh Block

## Slide 12: Plan for Post monsoon
Will collect all the wells monitored in pre-monsoon for data consistency
New wells and new locations to increase the coverage
This will provide additional analysis on
  Capturing water level fluctuation
  Rainfall-Recharge correlation
  Accuracy increase of Decision support tool (CLART)
  Help in water budgeting at village
  Water quality assessment (pilot)

## Slide 13: Protocols
At least one well per village
If possible choose upto 3 wells far apart from each other in the same village.
We should be able to measure these wells twice a year in the next few years.
If a well is dry, please note the total depth of the well so that we know up to what depth below ground there is no water.
Take the GPS measurement at the ground level and note the depth to water level also from this same point.
Measure water level in meters.
If there is a motor connected to the well, please ensure a minimum of 24 hrs gap between the motor being run and the depth being measured.
If you are equipped and experienced in measuring bore well depths then you are welcome to record depth of bore wells also. Otherwise, you can stick to open wells.
The data collection period is 12th October 2020 to 24th October 2020. In case the rain is ongoing in your location, please collect data 5 days after the rain stop

## Slide 14: PROCEDURE OF WELL MEASUREMENT
SOIL
ROCK1
ROCK2
DEPTH OF SOIL
DEPTH OF WATER LEVEL
Mobile
MEASURING TAPE
Do:
1. Put the GPS/Mobile on the ground
2. Measure the depth to water from the ground
Don’t:
Don’t put the Mobile on parapet wall
Don’t measure the depth from parapet wall
Parapet wall
Notes: 14

## Slide 15: PROCEDURE OF WELL MEASUREMENT
SOIL
ROCK1
ROCK2
DEPTH OF SOIL
DEPTH OF WATER LEVEL
Mobile
MEASURING TAPE
Do:
1. Put the GPS/Mobile on the ground
2. Measure the depth to water from the ground
Don’t:
Don’t put the Mobile on parapet wall
Don’t measure the depth from parapet wall
Notes: 15

## Slide 16
Ground Water Monitoring Tool

## Slide 17
Download the app from https://wmt.indiaobservatory.org.in
Press 3 seconds here to download the app
Press here to download

## Slide 18
User registration (One time only)
No Internet is required after registration
Once you select the district, you will be able to see the list of organization in that district,
if your organization name is not there, please select other and write the name

## Slide 19
Collection of Data
Click the + button
Check & enable GPS,
you can see the grid line
See the index for your location
(to know the ground water status)
Please zoom out to see the map

## Slide 20
Data collection in the existing well which has been monitored in premonsoon 2020
Click here to select village
Click on the well to see the details

## Slide 21
Click here to enter new water level
in the same well
1. If you are taking data from field,
please select “Actual”
2. If it is a training program, please select “Training”
3. If you want to test the tool, please select “Testing”

## Slide 22
Collection of Data from new well
Click the + button
Check & enable GPS
Take the data

## Slide 23
Collection of Data
Click the button to capture screen and location data

## Slide 24
Collection of Data
Fill up the form
Nos of Questions | Questions | Data input methods
Q1 | Screen capture and Location (Lat/Long/Alt) | Button press
Q2 | State-District-Block-Village | Dropdown
Q3 | Habitation Name | Text
Q4 | Name of the Well owner/well | Text
Q5 | Type of Well (Open/Bore) | Dropdown
Q6 | Does the well have water (Yes/No) | Dropdown
Q7 | If Yes- Depth to water, If No- Well depth | Text
Q8 | Photograph | Button press
Q9 | Water Quality | Dropdown & Text

## Slide 25
If you want to collect water quality data, please click here
Fill the data

## Slide 26
Submit the data
Click submit button to save the data in mobile
Click here to see the saved form
Select and Upload the form

## Slide 27
Click here to see the form after submission also
Data visualization after submission in mobile

## Slide 28
Data visualization after submission in portal
https://wmt.indiaobservatory.org.in
Temporary User id: guest
Password: guest2018

## Slide 29
Data visualization after submission in portal
https://wmt.indiaobservatory.org.in
Click here to see the forms
Click here to download data in pdf

## Slide 30
Data is also available in India Observatory Data Platform to correlate
with other 1800+ data layers of India’s Socio-Economic-Environmental parameters
https://dp.observatory.org.in

## Slide 31: Thank you
For instructions on how to use the android app and to know more about this initiative kindly refer to the documents in this link - https://www.indiaobservatory.org.in/tool/gmt
To download the app and contribute/visualize the data - register yourself and access the page - https://wmt.indiaobservatory.org.in/.
Write to us: support@indiaobservatory.org.in